## Slide 1: Demonstration of mass measurements at the Rare-RI Ring facility
June 28th, 2017
Saitama University
Shunichiro Omika
China-Japan collaboration workshop on “Nuclear mass and life for unravelling mysteries of r-process”
D. Nagae, Y. Abe, Y. Yamaguchi, F. Suzaki,
K. Wakayama, N. Tadano, R. Igosawa, K. Inomata, Y. Arakawa,
K. Nishimuro, T. Fujii, T. Mitsui, T. Yamaguchi, T. Suzuki,
S. Suzuki, T. Moriguchi, M. Amano, D. Kamioka, A. Ozawa,
S. Naimi, Z. Ge, Y. Yanagisawa, H. Suzuki, H. Baba, S. Michimasa,
S. Ota, G. Lorusso, Yu.A. Litvinov, M. Wakasugi, T. Uesaka, and Y. Yano

## Slide 2: Introduction
→
m/q : charge to mass ratio
T : revolution time
Index
0 : particle of reference
1 : particle of interest
Overview of Rare-RI Ring is presented by A. Ozawa
・Rare RI Ring is a device for the precise mass
measurements for short-lived nuclei.
・ The magnetic field in the ring is adjusted to
be isochronous by using trim coils.
・Rare RI Ring aims precision of mass determination
better than 10-6 with less than ～1 ms measurement time.
1/15
BigRIPS
SHARAQ
Rare-RI Ring
RIBF@RIKEN

## Slide 3: Commissioning experiments
2015
- First machine study (MS01) using 78Kr beam in June.
- Establishment of the self-trigger injection method.
- Succeeded in storage of single-ion.
- Confirmation of trim-coils effects after extraction.
→Extraction efficiency ~1%
- Second machine study (MS02) using 36Ar and 35Cl in Dec.
- Injection / Extraction of two nuclei in the same setting.
- Demonstrate the feasibility of mass measurement.
2016
- Third machine study (MS03) using 78Ge,77Ga,76Zn, etc. in Nov.
- Injection/Extraction many nuclei.
- Check the performance of R3.
2/15

## Slide 4: 3rd experiment setup
F3
F6
S0
PPAC
Pla
PPAC
IC
MCP + foil
ToF measurement
→ β determination
→Momentum determination
ELC
Pla
ToF measurement
→ Circulation time determination
Blue : PID@BigRIPS
Red : Extracted Events
F2
238U Beam @345MeV/u
From SRC
F0
Be Target
10 mm2
3/15
Pla

## Slide 5: Time of flight in Rare-RI Ring (S0 -> ELC)
701500
701480
701460
701440
701420
701400
40
30
20
0
10
The Isochronous filed of R3 is tuned by 78Ge with 175 MeV/nucleon.
77Ga
78Ge
79As
701350
701400
701550
701650
701700
701750
701500
701450
701600
0.0
0.2
0.4
-0.2
-0.4
momentum@F6 [%]
ToFS0->ELC [ns]
ToFS0->ELC [ns]
Count
4/15
Preliminary
78Ge

## Slide 6: Circulation time
S0
ELC
RI Beam
From BigRIPS
・First, we decide a circulation number (N) of reference particle.
This N is calculated by MCP data that is inserted ring.
・The injection line is not isochronous magnetic filed.
But, we approximate circulation start from S0 and stop to ELC.
→Next, we decide circulation numbers of
another particles using below relationship.
MCP + foil
5/15

## Slide 7: Correction circulation time
Correction circulation time
79As
75Cu
76Zn
77Ga
78Ge
1
10
102
365
385
380
375
370
390
395
Correction circulation time [ns]
Count
389.52
389.48
389.44
389.40
389.36
-0.5
0
0.5
396.02
395.98
395.94
395.90
395.86
-0.5
0
0.5
Circulation time [ns]
Correction circulation time [ns]
RMS
0.010 [ns]
RMS
0.0057 [ns]
Correction
momentum@F6 [%]
momentum@F6 [%]
Ex)75Cu
6/15

## Slide 8: m/q spectrum
In this talk, definition ‘Accuracy’ as | (m/qexp-m/qAME2012) / m/qAME2012 |
About particles close to the nucleus as a reference,
‘Accuracy’ achieve ～10-6
0
0.08
0.12
0.16
0.2
0.04
2
4
0
6
77Ga m/q – 2.48
Count
AME2012
2.4810389
Ex) 77Ga
7/15
Preliminary

## Slide 9: Error estimation
・ From T1 value
Width of m/q spectrum. ( Width of correction circulation time)
・ From beta calibration
The uncertainty of beta calibration is treated as an error.
・ From T0 value
In analysis, T0 value is put the fixed value.
We treat the width of T0 as the uncertainty of this value.
8/15
++

## Slide 10: Error from correction T1
0
0.08
0.12
0.16
0.2
0.04
2
4
0
6
77Ga m/q – 2.48
Count
Ex) 77Ga
The width of m/q spectrum is reflected
the width of correction circulation time.
We define σT1 as RMS / m/qexp .
9/15
Preliminary

## Slide 11: Error from uncertainty of beta
F3
S0
D3
4.8575 Tm
D4
4.8476 Tm
D5
4.8477 Tm
D-H7
4.8467 Tm
D-H8
4.8472 Tm
Average Brho
4.84934 [Tm]
RMS of Brho
0.00410 [Tm]
We calibrate beta by ToFF3->S0 and Brho.
But, Brho value has deviation.
An error from uncertainty of Brho means
an uncertainty beta calibration.
We evaluate this error as how change m1/q1
using average Brho or Brho + δBrho.
10/15

## Slide 12: Error from uncertainty of T0
373.0
373.04
373.12
373.16
373.08
373.2
4
3
2
1
0
78Ge Circulation time [ns]
Count
To calculate m1/q1, T0 is fixed value.
An Error from uncertainty of T0 is
estimated by changing T0 value, and
Check how much change m1/q1.
11/15
Preliminary

## Slide 13: For future experiment
・ Improvement Brho error
→ To calculate beta, measure transport matrix elements and
decide path length by trajectory reconstruction.
(In MS03 experimental setup, we can’t reconstruction)
・ Improvement efficiency
→ In MS03, extraction efficiency is ～0.1% (comparison F3 events).
To increase efficiency, tuning of injection line more optimum.
・Improvement ToF counter
→ S. Suzuki Talk
For improvement above problem,
We are developing the position sensitive MCP + Foil detector.
13/15

## Slide 14: Summary
・3rd commissioning experiment has been done
to check the performance of Rare-RI Ring.
・As a reference particle for isochronous field, we used 78Ga@175MeV/nucleon.
・The isochronous filed in ring achieve 5.0×10-6 .
・In particles close to the nucleus as a reference, ‘Accuracy’ achieve ～10-6.
・Precision is ～10-5.
14/15